## Slide 1: Day 2: Primary Pollutants
Air Pollution

## Slide 2: Primary Pollutants
Pollutants put directly into the air
Causes of Primary Pollutants – factories, cars, wind and soil, volcanoes, forest fires, pollen, decaying plants, salt particles from the sea, and refrigerants.

## Slide 3: AIR POLLUTION
Some primary air pollutants may react with one another or with other chemicals in the air to form secondary air pollutants.
Notes: *

## Slide 4: Major Primary Pollutants:CO2
Carbon oxides:
  Carbon monoxide (CO) is a highly toxic gas that forms during the incomplete combustion of carbon-containing materials.
  Causes: Incomplete combustion of gasoline & natural gas
  93% of carbon dioxide (CO2) in the troposphere occurs as a result of the carbon cycle.
  Causes: Burning of fossil fuels such as coal
  7% of CO2 in the troposphere occurs as a result of human activities
    It is not regulated as a pollutant under the U.S. Clean Air Act.
Notes: *

## Slide 6: Major Primary Pollutants: NOx
Nitrogen oxides
  Nitrogen oxide (NOx) forms when nitrogen and oxygen gas in air react at the high-combustion temperatures in automobile engines and coal-burning plants. (cause)
  NOx can also form from lightning and certain soil bacteria.
Notes: *

## Slide 8: Major Primary Pollutants: SO2
Sulfur dioxide (SO2):
  About one-third of SO2 in the troposphere occurs naturally through the sulfur cycle.
  Two-thirds come from human sources, mostly combustion (S+ O2 → SO2) of sulfur-containing coal and from oil refining and smelting of sulfide ores.
Notes: *

## Slide 9: Major Primary Pollutants: SPM
Suspended particulate matter (SPM):
  Consists of a variety of solid particles and liquid droplets small and light enough to remain suspended in the air.
  The most harmful forms of SPM are fine particles (PM-10, with an average diameter < 10 micrometers) and ultrafine particles (PM-2.5).
  According to the EPA, SPM is responsible for about 60,000 premature deaths a year in the U.S.
Notes: *

## Slide 10: Major Primary Pollutants: VOCs
Volatile organic compounds (VOCs):
  Most are hydorcarbons emitted by the leaves of many plants and methane.
  About two thirds of global methane emissions comes from human sources such as burning of wood & gas and personal care products such as perfume, hair spray, paints, cleaning agents
  Other VOCs include industrial solvents such as trichlorethylene (TCE), benzene, and vinyl chloride.
    Long-term exposure to benzene can cause cancer, blood disorders, and immune system damage.
Notes: *

## Slide 11: Major Primary Pollutants: Rn
Radon (Rn):
  Is a naturally occurring radioactive gas found in some types of soil and rock.
  It can seep into homes (basements) and buildings sitting above such deposits.
Notes: *

## Slide 12
Copy this in your notes!