## Slide 1: Water Pollution

## Slide 2: Water Pollution Types
Pathogens/Sewage
Organic Wastes
Inorganic Chemicals
Sediments
Nutrients
Thermal
Oil Spills
Radioactive

## Slide 3: Pathogens Carried by Sewage
Disease-causing agents
Safety measures
  Purification of public water supply
  Sanitary collection/treat-ment of sewage
  Sanitary practices when processing food

## Slide 4
  scientists monitor water quality by using bacterial counts, chemical analysis, and indicator organisms
    number of colonies of fecal coliform bacteria present in a water sample
      drinking water: 0 colonies/100 mL
      swimming water: < 200 colonies/100 mL
Infectious Agents:

## Slide 5: Organic Wastes
Dissolved oxygen (DO) in the water is depleted during decomposition of organic wastes.
Water quality test:
  Biochemical oxygen demand (BOD): measure of the amount of organic material.

## Slide 6: Chemical Pollutants
Inorganic chemicals
  Heavy metals, acids, road salts
Organic chemicals
  Petroleum, pesticides, detergents

## Slide 7: Effect of Sediments on Streams
Loss of hiding/resting places for small fish
Attached aquatic organisms scoured from the rocks and sand
Poor light penetration
(increased turbidity)

## Slide 9: Different Kinds of Aquatic Plants
Benthic plants
  Plants rooted underwater
  May stick out of the water or be completely submerged
Phytoplankton
  Algae & free floating plants
  May be single celled or long filaments

## Slide 11: The Impacts of Nutrient Enrichment
Oligotrophic: nutrient-poor water
  Mostly benthic plants
Eutrophic: nutrient-rich water
  Mostly phytoplankton

## Slide 13: Eutrophication
As nutrients are added from pollution, an oligotrophic condition rapidly becomes eutrophic.
Oligotrophic
Eutrophic

## Slide 14: Eutrophic or Oligotrophic?
High dissolved O2
Deep light penetration
High phytoplankton
Turbid waters
High species diversity
Good recreational qualities
High detritus decomposition

## Slide 15: Eutrophic or Oligotrophic?
Low bacteria decomposition
Benthic plants
Warm water
High nutrient concentration
High BOD
High sediments

## Slide 16: Combating Eutrophication
Attack the symptoms
  Chemical treatment
  Aeration
  Harvesting aquatic weeds
  Drawing water down
Getting at root cause
  Controlling point sources
  Controlling non-point sources

## Slide 18: Thermal Pollution: Causes decrease in DO
  Coal Powerplants: Heats water to steam to turn turbines then uses cooling tower to condense water. Water is 10oC hotter when put back into the lake.
  Urban Stormwater Runoff: Surfaces like parking lots and sidewalks heat up. When it rains, water absorbs heat and is put into bodies of water
  Deforestation: Forests & vegetation reflect back & absorb sun’s heat. Deforestation leaves the water sources directly exposed to sunlight!

## Slide 19: Oil Spills
Can clog the blowholes of whales & dolphins so that they can’t breathe or communicate
Coats the fur of otters and seals which can cause hypothermia
When it washes into coastal marshes, mangrove forests or other wetlands, it damages the plants & makes area unsuitable for wildlife

## Slide 20: Radioactive
Relates to Thermal Pollution
Water is used to cool the control rods. Warm water is put back into lake which causes dissolved oxygen to decrease.

## Slide 21: Homework
Research a case of eutrophication.
Include:
Source of the pollution
Area (size) affected
Map showing the location
Pictures of the problem
How was it solved

## Slide 22: Slide Title
Make Effective Presentations
Using Awesome Backgrounds
Engage your Audience
Capture Audience Attention

## Slide 23: Slide Title
Make Effective Presentations
Using Awesome Backgrounds
Engage your Audience
Capture Audience Attention

## Slide 24: Slide Title
Product A
Feature 1
Feature 2
Feature 3
Product B
Feature 1
Feature 2
Feature 3